## Slide 1
Introduction to
Seismic Waveform Inversion Toolbox-1.0
Haipeng Li @ USTC
July 2021

## Slide 2
Structures of SWIT
Haipeng Li & Junlun Li, in preparation

## Slide 3
Installation of SWIT

## Slide 4
Installation of SWIT

## Slide 5
Installation of SWIT

## Slide 6
1. Input Parameters
2. Viewing Window
3. Viewing Options
3. Functions
4. Output Histories
6. System Status

## Slide 7
Project working folder
CPU number for MPI
Figure aspect for plotting
Save parameters in file
Load previously saved parameter file
Parameters for System

## Slide 8
Model size along x direction
Temporal step (in s)
Model size along z direction
Grid size (in m)
Total time steps
PML size, use a relatively large one, i.e., 50
Set free surface or not
Field-data path, data should be named as: src1_sg.su, src2_sg.su, ..., src40_sg.su, ...
True Vp model saved in the txt file
Initial Vp model saved in the txt file
Synthetic FWI requires: Vp true & Vp init
Field-data application requires: Vp init & SU data
Parameters for Model

## Slide 9
Receiver file, see examples for detailed format
Source file, see examples for detailed format
Acqusition type: land or marine
Source wavelet: Ricker or from file
If from file, set the file path
If Ricker, set the dominant frequency
Parameters for Acquisition

## Slide 10
Set misfit function: Waveform, Traveltime, etc.
Set optimization scheme: NLCG or L-BFGS (NLCG is recommended)
Set step length, i..e, 0.01 or 0.02 (with respect to Vp model)
Set gradient mute. In marine case, it’s the water layer size; in land case, set as ~10 (in grid)
Set gradient smoothing size, i.e., 10 (in grid)
Set the time window after the first break, i.e., 1.0 (in s)
Set the distance to mute near offset distance (in m)
Set number of iteration
Minimum Vp (in m/s)
Maximum Vp (in m/s)
Set whether to normalize the data. If so, set which type
Set whether to filter the data. If so, set which type
Set the low frequency bound (in Hz)
Set the high frequency bound (in Hz)
Set whether to mute late arrivals based on the automatically picked first break
Set whether to mute traces of near offset
Set whether to mute far offset
Set the distance to mute traces of far offset distance (in m)
Parameters for Inversion

## Slide 11
View a txt file (donot require nx & nz) or binary file (require nx & nz)
Convert a binary file to a txt file (require nx & nz)
Smooth a txt file. sp: the smoother radius; mt: the top mute for any water layer
Forward: Run forward modeling on the provided true model to generate the synthetic dataset
FWI: Run FWI and the initial model and the SU data should be both prepared.
Clear: clear the output histories
Functions
For syn-model FWI: provide Vp true & Vp init. Run Forward and then run FWI
For field-data FWI: provide Vp init & SU data. Run FWI

## Slide 12
SWIT solves the variable-density acoustic wave equation in the stress-velocity form;
SWIT uses a 4th-order Butterworth filter (zero-order);
SWIT mutes the late arrivals based on the automatically picked first break in a brutal way;
SWIT does not support the arbitrary arrangement of receivers for different sources yet.
Other issues